## Slide 1
Electronics I – Fall 2018
CHAPTER 3

## Slide 2
Devotional
DO YOU TRULY BELIEVE
“I do believe; help me overcome my unbelief”
(Mark 9:24)
How solid is your faith? Have you reduced it to outward matters of attending church, singing songs of praise, listening to nice sermons and trying to live a respectable life?
Your faith only becomes reality when the external ceremonies of Christianity become a pulsating and powerful experience in your soul. It becomes a reality when you no longer see yourself as someone defeated by sin because God’s wholly spirit, who resides in you, enables you to triumph over all sin.
You must develop the discipline of experiencing Christ’s presence in your everyday life. Prayer, Bible study and fellowship with other believers are essential to attaining a positive living and dynamic faith.

## Slide 3
The Lord’s Prayer
Our Father, which art in heaven, Hallowed be thy Name. Thy Kingdom come. Thy will be done in earth, As it is in heaven.
Give us this day our daily bread. And forgive us our trespasses, As we forgive them that trespass against us. And lead us not into temptation, But deliver us from evil.
For thine is the kingdom,
The power, and the glory,
For ever and ever.
Amen.

## Slide 4
Quote of the day
“The Simple Path Silence is Prayer Prayer is Faith Faith is Love Love is Service The Fruit of Service is Peace”
― Mother Teresa

## Slide 5: Chapter #3: Semiconductors
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 6: Introduction
IN THIS CHAPTER WE WILL LEARN:
  The basic properties of semiconductors and, in particular, silicone – the material used to make most modern electronic circuits.
  How doping a pure silicon crystal dramatically changes its electrical conductivity – the fundamental idea in underlying the use of semiconductors in the implementation of electronic devices.

## Slide 7: Introduction
IN THIS CHAPTER WE WILL LEARN:
  The two mechanisms by which current flows in semiconductors – drift and diffusion charge carriers.
  The structure and operation of the pn junction – a basic semiconductor structure that implements the diode and plays a dominant role in semiconductors.

## Slide 8: Introduction
The valence electrons are the electrons in the outermost electron shell of an atom.
Valence electrons participates in the formation of chemical bonds.
The valence electrons are less tightly bound and easier to remove, because they are farther away from the nucleus of the atom.
Elements whose atoms have the same number of valence electrons are grouped together in the Periodic Table.

## Slide 9: Introduction

## Slide 10: Introduction
Periodic table group | Valence electrons
Group 1 (I) (alkali metals) | 1
Group 2 (II) (alkaline earth metals) | 2
Groups 3-12 (transition metals) | 3–12*
Group 13 (III) (boron group) | 3
Group 14 (IV) (carbon group) | 4
Group 15 (V) (pnictogens or nitrogen group) | 5
Group 16 (VI) (chalcogens or oxygen group) | 6
Group 17 (VII) (halogens) | 7
Group 18 (VIII or 0) (noble gases) | 8**

## Slide 11: Introduction
The most reactive kind of metallic element is a metal from Group 1 (e.g., sodium or potassium).
An atom in Group 1 has only a single valence electron.
This one valence electron is easily lost to form a positive ion (e.g., Na+ or K+)
Atoms with one or two valence electrons are highly reactive because the extra valence electrons are easily removed to form positive ions.

## Slide 12: Introduction
Thus, valence electrons are also responsible for the electrical conductivity of an element
As a result, an element may be classified as a metal, a nonmetal, or a semiconductor (or metalloid).
Metals have high electrical conductivity and they are good conductors of electricity
Non metals have low electrical conductivity; it acts as an insulator.
A semiconductor has an electrical conductivity that is between that of a metal and a nonmetal

## Slide 13: Introduction
Valence Electron: Definition, Configuration & Example - Video & Lesson Transcript | Study.com

## Slide 14: Conductors & Insulators
In a conductor, electric current can flow freely
In an insulator electric curent cannot flow
Metals such as copper typify conductors
While most non-metallic solids are said to be good insulators
Because they have extremely high resistance to the flow of charge through them.

## Slide 15: Conductors & Insulators
"Conductor" implies that the outer electrons of the atoms are loosely bound and free to move through the material.
Most atoms hold on to their electrons tightly and are insulators.
In copper, the valence electrons are essentially free and strongly repel each other.
Any external influence which moves one of them will cause a repulsion of other electrons which propagates, "domino fashion" through the conductor.

## Slide 16: 3.1. Intrinsic Semiconductors
Covalent bond – is a form of chemical bond in which two atoms share a pair of electrons.
  It is a stable balance of attractive and repulsive forces between atoms when they share electrons.

## Slide 17: 3.1. Intrinsic Semiconductors
Silicon atom
  four valence electrons
  each pair of shared valence electrons forms a covalent bond
  the atoms form a lattice structure

## Slide 18: 3.1. Intrinsic Semiconductors
Figure 3.1 Two-dimensional representation of the silicon crystal.
The circles represent the inner core of silicon atoms
with +4 indicating its positive charge of +4q,
which is neutralized by the charge of the four valence electrons.
Observe how the covalent bonds are formed by sharing of the valence electrons.
At 0K, all bonds are intact and no free electrons are available for current conduction.

## Slide 19: 3.1. Intrinsic Semiconductors
silicon at low temperatures
  all covalent bonds – are intact
  no electrons – are available for conduction
  conductivity – is zero

## Slide 20: 3.1. Intrinsic Semiconductors
silicon at room temp
  some covalent bonds – break, freeing an electron and creating hole, due to thermal energy
  some electrons – will wander from their parent atoms, becoming available for conduction
  conductivity – is greater than zero
The process of freeing electrons, creating holes, and filling them facilitates current flow…

## Slide 21: 3.1: Intrinsic Semiconductors
At room temperature
Some of the covalent bonds are broken by thermal generation.
Each broken bond gives rise to a free electron and a hole
Both of which become available for current conduction.

## Slide 22: 3.1. Intrinsic Semiconductors
Intrinsic semiconductor – is one which is not doped
Not being doped means that the basic properties of the semi conductor are not affected
  One example is pure silicon.
Generation – is the process of free electrons and holes being created.
  generation rate – is speed with which this occurs.

## Slide 23: 3.1. Intrinsic Semiconductors
Recombination – is the process of free electrons and holes disappearing.
For the most part, free electrons are typically recombining.
  recombination rate – is speed with which this occurs.
Generation may be effected by thermal energy.
As such, both generation and recombination rates will be (at least in part) a function of temperature.

## Slide 24: 3.1. Intrinsic Semiconductors
Generation – is the process of free electrons and holes being created.
Recombination – is the process of free electrons and holes disappearing.
Both generation and recombination can be affected by temperature
Now we need a way to mathematically describe the movement of electrons and holes inside of a crystal

## Slide 25: 3.1. Intrinsic Semiconductors
In thermal equilibrium, the behavior below applies…
  ni = number of free electrons and holes / unit volume
  p = number of holes
  n = number of free electrons

## Slide 26: 3.1. Intrinsic Semiconductors
ni = number of free electrons and holes in a unit volume for intrinsic semiconductor
B = parameter which is 7.3E15 cm-3K-3/2 for silicon
T = temperature (K)
Eg = bandgap energy which is 1.12eV for silicon
k = Boltzman constant (8.62E-5 eV/K)

## Slide 27: 3.1. Intrinsic Semiconductors
Eg = bandgap energy which is 1.12eV for silicon

## Slide 28: 3.1. Intrinsic Semiconductors
Q: Why can thermal generation not be used to effect meaningful current conduction?
  A: Silicon crystal structure described previously is not sufficiently conductive at room temperature.
    Additionally, a dependence on temperature is not desirable.
Q: How can this “problem” be fixed?
  A: doping

## Slide 29: Semiconductor Doping
Doping – is the intentional introduction of impurities into an extremely pure (intrinsic) semiconductor for the purpose changing carrier concentrations.
In general, an increase in doping concentration affords an increase in conductivity due to the higher concentration of carriers available for conduction.

## Slide 30: Semiconductor Doping
Degenerate (very highly doped) semiconductors have conductivity levels comparable to metals and are often used in modern integrated circuits as a replacement for metals.
Often superscript plus and minus symbols are used to denote relative doping concentration in semiconductors.

## Slide 31: Semiconductor Doping
Doping a semiconductor in a good crystal introduces allowed energy states within the band gap
But these energy states are very close to the energy band that corresponds to the dopant type.
In other words,
Electron donor impurities create states near the conduction band
While electron acceptor impurities create states near the valence band.

## Slide 32: Semiconductor Doping
The gap between these energy states and the nearest energy band is usually referred to as dopant-site bonding energy or EB and is relatively small.
For example, the EB for Boron in silicon bulk is 0.045 eV, compared with silicon's band gap of about 1.12 eV.

## Slide 33: 3.2. Doped Semiconductors
p-type semiconductor
  Silicon is doped with element having a valence of 3.
  To increase the concentration of holes (p).
  One example is boron, which is an acceptor.
n-type semiconductor
  Silicon is doped with element having a valence of 5.
  To increase the concentration of free electrons (n).
  One example is phosophorus, which is a donor.

## Slide 34: 3.2. Doped Semiconductors
p-type semiconductor
  Silicon is doped with element having a valence of 3.
  To increase the concentration of holes (p).
  One example is boron.
n-type semiconductor
  Silicon is doped with element having a valence of 5.
  To increase the concentration of free electrons (n).
  One example is phosophorus, which is a donor.
Acceptor  Can accept
one more valence electron
Donor  Can donate
one more valence electron

## Slide 35: 3.2. Doped Semiconductors
ni = number of free electrons and holes / unit volume
n-type doped semiconductor
  If ND (the number of donors) is much greater than ni …
    concentration of donor atoms is ND
  Then the concentration of electrons in the n-type is defined as in (3.4).

## Slide 36: 3.2. Doped Semiconductors
ni = number of free electrons and holes / unit volume
p-type doped semiconductor
  If NA (the number of acceptors) is much greater than ni
    concentration of acceptor atoms is NA
  Then the concentration of holes in the p-type is defined as in (3.6).

## Slide 37: 3.2. Doped Semiconductors
The key is that the number of free electrons (n- or p-type) is dependent on doping concentration, not temperature…
Anytime a doping volume becomes greater than the overall concentration of ions ni, the semi-conductor material takes the properties of the doping material
If doping volume is p-type semi- conductor becomes p-type
If doping volume is n-type semi-conductor becomes n-type
Both doping types can set movement of charges holes or electrons via Diffusion

## Slide 38: 3.3.1. Drift Current
Q: What happens when an electrical field (E) is applied to a p-type or n-type semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are repelled.
Q: What happens when an electrical field (E) is applied to a n-type semiconductor crystal?
  A: Electrons are accelerated in the direction of E, free holes are repelled.

## Slide 39: 3.3.1. Drift Current
Q: How are the velocity of these holes and electrons defined?
  A: Defined in function of their mobility μ

## Slide 40: 3.3.1. Drift Current
Q: What happens when an electrical field (E) is applied to a semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are repelled.
Q: How is the velocity of these holes defined?
.E (volts / cm)
.mp (cm2/Vs) = 480 for silicon
.mn (cm2/Vs) = 1350 for silicon
note that electrons move much faster - with velocities 2.5 times higher than holes

## Slide 41: 3.3.1. Drift Current
Figure 3.5: An electric field E established in a bar of silicon causes the holes to drift in the direction of E and the free electrons to drift in the opposite direction. Both the hole and electron drift currents are in the direction of E.

## Slide 42: 3.3.2. Diffusion Current
Carrier diffusion – is the flow of charge carriers from area of high concentration to low concentration.
  Meaning the tendency to achieve equilibrium
  This flow of charges creates a current called diffusion current
Diffusion current – is the current flow that results from carrier diffusion.

## Slide 43: 3.3.2. Diffusion Current
Take the following example…
  inject holes – By some unspecified process, one injects holes in to the left side of a silicon bar.
Figure 3.6: A bar of silicon (a) into which holes are injected, this creates a movement of holes along the x axis

## Slide 44: 3.3.2. Diffusion Current
  concentration profile arises – Because of this continuous hole inject, a concentration profile arises.
  diffusion occurs – Because of this concentration gradient, holes will flow from left to right.
Figure 3.6: (b). The holes diffuse in the positive direction of x and give rise to a hole-diffusion current in the same direction.

## Slide 45: 3.3.3. Relationship Between D and m.?
Q: What is the relationship between diffusion constant (D) and mobility (m)?
  A: thermal equilibrium voltage (VT)
Q: What is the value of VT?
  A: at T = 300K, VT = 25.9mV
known as Einstein Relationship

## Slide 46: Drift and Diffusion Currents
Thus far, we have looked at two types of currents
  Drift current density (Jdrift)
    effected by – an electric field (E).
  Diffusion current density (Jdiff)
    effected by – concentration gradient (or changes in concentration) in free electrons and holes.
Let us now define Diffusion Current

## Slide 47: 3.3.2. Diffusion Current
Q: How is diffusion current defined?

## Slide 48: Drift and Diffusion Currents
Thus far, we have defined Diffusion and Drift Currents
Diffusion currents are born due to a variation in concentration of charges in a cross section of a body
Drift currents are born due to the application of an electric field to a cross section of a body
Both Drift and Diffusion currents will change the distribution of the energy band of a body
The change in energy band distribution will in turn change the electrical conductivity of the body – thereby making it either accept or donate an ion

## Slide 49: 3.3.2. Fermi Level
The Fermi level of a body expresses the work required to add to or remove an electron from the body.
Therefore, VA − VB, the observed difference in voltage between two points, A and B, in an electronic circuit is exactly related to the corresponding chemical potential difference, µA − µB, in Fermi level by the formula:
where −e is the electron charge

## Slide 50: 3.3.2. Fermi Level
From the formula, we can see that electrons will move from a body of high mobility µ (low voltage) to low mobility µ (high voltage) if a simple path is provided.
This flow of electrons will cause the lower µ to increase (due to charging or other repulsion effects) and likewise cause the higher µ to decrease.
This also means that the voltage (measured with a voltmeter) between any two points across a body will be zero, at equilibrium (or when µA=µB).

## Slide 51: 3.3.2. Fermi Level
In the band theory of solids, electrons are considered to occupy a series of bands composed of single-particle energy eigenstates each labelled by ϵ.
The Fermi–Dirac distribution, gives the probability that (at thermodynamic equilibrium) a state having energy ϵ is occupied by an electron

## Slide 52
Fermi Dirac distribution
T is the absolute temperature and k is Boltzmann's constant.
If there is a state (energy band) at the Fermi level (ϵ = µ), then this state will have a 50% chance of being occupied.
3.3.2. Fermi Level

## Slide 53: 3.3.2. Fermi Level
Fermi-Dirac distribution vs. energy, with μ = 0.55 eV and for various temperatures in the range 50K ≤ T ≤ 375K

## Slide 54: Workshop Exercises
Exercise 1
Calculate the drift current density J=σE for silicon at T = 300 K doped
with arsenic atoms at a concentration of Nd = 8 × 1015 cm−3 .
Assume mobility values of μn = 1350 cm2/V–s and μp = 480 cm2/V–s.
Assume the applied electric field is 100 V/cm.
The electron and hole concentrations are:

## Slide 55: Workshop Exercises
And
Because of the difference in magnitudes between the two
concentrations, the conductivity is given by
Or
Then the drift current density is

## Slide 56: Workshop Exercises
Note: As the impurity concentration increases, the mobility values will
decrease.
This effect means that the conductivity given by
is not a linear function of impurity doping.
These factors are important in the design of semiconductor
devices, but will not be considered in detail in this chapter.

## Slide 57: Workshop Exercises
Exercise 2
Calculate the diffusion current density Jn for a given semiconductor.
Consider silicon at T = 300 K.
Assume the electron concentration varies linearly from n = 1012 cm−3 to
n = 1016 cm−3 over the distance from x = 0 to x = 3 μm. Assume Dn = 35
cm2/s.

## Slide 58: Workshop Exercises
Exercise 2
We have

## Slide 59: Workshop Exercises
Notes
In the previous example, a current density on the order of 200 A/cm2 was calculated.
This implies that for a current of I = 1 mA = 1 × 10−3 A and J = 200 A/cm2, the cross-sectional area is: S = (1 × 10−3 /200)= 5 × 10−6 cm2.
This simple calculation shows why semiconductor devices can be very small in size, one of the greatest advantages of this technology.

## Slide 60: 3.4.1. Physical Structure
pn junction structure
  p-type semiconductor
  n-type semiconductor
  metal contact for connection
Figure 3.8: Simplified physical structure of the pn junction.
(Actual geometries are given in Appendix A.). As the pn junction implements the junction diode, its terminals are labeled anode and cathode.

## Slide 61: 3.4.2. Operation with Open-Circuit Terminals
Q: What is the state of pn junction with open-circuit terminals?
A: p-type material contains majority of holes
    these holes are neutralized by equal amount of bound negative charge
  n-type material contains majority of free electrons
    these electrons are neutralized by equal amount of bound positive charge

## Slide 62: 3.4.2. Operation with Open-Circuit Terminals
Bound charge
  charge of opposite polarity of a given material
  neutralizes the electrical charge of these majority carriers
  does not affect concentration gradients

## Slide 63
Q: What happens when a pn-junction is newly formed – aka., when the p-type and n-type semiconductors first touch one another?
  A: See following slides…
3.4.2. Operation with Open-Circuit Terminals

## Slide 64: Step #1: The p-type and n-type semiconductors are joined at the junction.
Figure: The pn junction with no applied voltage
(open-circuited terminals).
n-type semiconductor filled with free electrons
p-type semiconductor filled with holes
junction

## Slide 65: Step #1A: (a) Bound charges are attracted (from environment) by free electrons and holes in the p-type and n-type semiconductors, respectively.
Figure: The pn junction with no applied voltage (open-circuited terminals).
positive bound charges
negative bound charges
(b) They remain weakly “bound” to these majority carriers; however, they do not recombine.

## Slide 66: Step #2: Then Diffusion begins. In this process, those free electrons and holes which are closest to the junction will recombine and, essentially, eliminate one another.
Figure: The pn junction with no applied voltage (open-circuited terminals).

## Slide 67: Step #3: As diffusion occurs and free electrons recombine with holes a Depletion region begins to form
Then, the Depletion region is filled with “uncovered” charges – who have lost the majority carriers to which they were linked.
Figure: The pn junction with no applied voltage (open-circuited terminals).

## Slide 68: 3.4.2. Operation with Open-Circuit Terminals
Q: Why does diffusion occur even when bound charges neutralize the electrical attraction of majority carriers to one another?
  A: Diffusion current, as shown in (3.19) and (3.20), is effected by a gradient in concentration of majority carriers
  Therefore the movement of unbounded majority carriers creates a diffusion current

## Slide 69: Step #4: (a) Eventually, the “uncovered” charges effect a voltage differential across the depletion region. (b) The magnitude of voltage differential grows, as diffusion continues and becomes a barrier voltage (V0)
voltage potential
location (x)
barrier voltage (Vo)
No voltage differential exists across regions of the pn-junction outside of the depletion region because of the neutralizing effect of positive and negative bound charges.

## Slide 70: Step #5: The barrier voltage (V0) is an electric field whose polarity opposes the direction of diffusion current (ID). As the magnitude of V0 increases, the magnitude of ID decreases.
Figure: The pn junction with no applied voltage (open-circuited terminals).
diffusion current (ID)
drift current (IS)

## Slide 71: Step #6: Equilibrium is reached when (a) diffusion ceases (b) once the magnitudes of diffusion and drift currents equal one another – resulting in no net flow.
diffusion current (ID)
drift current (IS)
Once equilibrium is achieved, no net current flow exists (Inet = ID – IS) within the pn-junction while
under open-circuit condition.
p-type
n-type
depletion region

## Slide 72: 3.4.2. Operation with Open-Circuit Terminals
pn-junction built-in voltage (V0) – is the equilibrium value of barrier voltage.
  It is defined in (3.22) below
  Generally, it takes on a value between 0.6 and 0.9V for silicon at room temperature.
  This voltage is applied across depletion region, not terminals of pn junction.
    Power cannot be drawn from V0.

## Slide 73: 3.4.2. Operation with Open-Circuit Terminals
pn-junction built-in voltage (V0) – is the equilibrium value of barrier voltage.
This primary equilibrium comes from doping effects only

## Slide 74: 3.5.1. Qualitative Description of Junction Operation
Figures to right will show the pn-junction for three different conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) forward bias – dc voltage VF is applied – barrier shrinks
  (c) reverse bias – dc voltage VR is applied – barrier widens
Figure 3.11: The pn junction in:
(a) equilibrium; (b) forward bias
(c) reverse bias;.

## Slide 75
Figure to right shows pn-junction under three conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) reverse bias – where a dc voltage VR is applied.
  (c) forward bias – where a dc voltage VF is applied.
Figure 3.11: The pn junction in: (a) equilibrium; (b) reverse bias; (c) forward bias.
1) no voltage applied
2) voltage differential across depletion zone is V0
3) ID = IS
1) negative voltage applied
2) voltage differential across depletion zone is V0 + VR
3) ID < IS
1) positive voltage applied
2) voltage differential across depletion zone is V0 - VF
3) ID > IS

## Slide 76: 3.5.1. Qualitative Description of Junction Operation
Reverse bias case
  the externally applied voltage VR adds to (aka. reinforces) the barrier voltage V0
    increase effective barrier
  this reduces rate of diffusion, reducing ID
    if VR > 1V, ID will fall to 0A
  the drift current IS is unaffected, but dependent on temperature
  result is that pn junction will conduct small drift current IS
Forward bias case
  the externally applied voltage VF subtracts from the barrier voltage V0
    decrease effective barrier
  this increases rate of diffusion, increasing ID
  the drift current IS is unaffected, but dependent on temperature
  result is that pn junction will conduct significant current ID - IS
minimal current flows in reverse-bias case
significant current flows in forward-bias case

## Slide 77: Workshop Exercises
Exercise 5
Calculate the built-in potential barrier of a pn junction.
Consider a silicon pn junction at T = 300 K, doped at Na = 1016 cm−3 in
the p-region and Nd = 1017cm−3 in the n-region. From the results of
Example 1.1, we have ni = 1.5 × 1010cm−3 for silicon at room
temperature.
We then find:

## Slide 78: Workshop Exercises
Exercise 5
Comment: Because of the log function, the magnitude of Vbi is not a
strong function of the doping concentrations.
Therefore, the value of Vbi for silicon pn junctions is usually within 0.1
to 0.2 V of this calculated value.

## Slide 79: Workshop Exercises
Exercise 6
Calculate Vbi for a GaAs pn junction at T = 300 K for Na = 1016
cm−3 and Nd = 1017 cm−3 (b) Repeat part (a) for a Germanium pn
junction with the same doping concentrations. (Ans. (a) Vbi = 1.23
V, (b) Vbi = 0.374 V).
To Try at home

## Slide 80: Workshop Exercises
Exercise 6
The potential difference, or built-in potential barrier, across the space-
charge region cannot be measured by a voltmeter because new
potential barriers form between the probes of the voltmeter and the
semiconductor, canceling the effects of Vbi .
In essence, Vbi maintains equilibrium, so no current is produced by this
voltage. However, the magnitude of Vbi becomes important when we
apply a forward-bias voltage.

## Slide 81: Workshop Exercises
Exercise 7
Calculate the junction capacitance of a pn junction.
Consider a silicon pn junction at T = 300 K, with doping concentrations
of Na = 1016 cm−3 and Nd = 1015 cm−3. Assume that ni = 1.5 × 1010
cm−3 and let Cjo = 0.5 pF. Calculate the junction capacitance at VR =
1V and VR = 5V.
The built-in potential is determined by

## Slide 82
Figure to right shows pn-junction under three conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) reverse bias – where a dc voltage VR is applied.
  (c) forward bias – where a dc voltage VF is applied.
Figure 3.11: The pn junction in: (a) equilibrium; (b) reverse bias; (c) forward bias.
1) no voltage applied
2) voltage differential across depletion zone is V0
3) ID = IS
1) negative voltage applied
2) voltage differential across depletion zone is V0 + VR
3) ID < IS
1) positive voltage applied
2) voltage differential across depletion zone is V0 - VF
3) ID > IS

## Slide 83: Forward-Bias Case
From the previous slide, we know that decreased junction barrier voltage will be accompanied by…
  (1) decrease in stored uncovered charge on both sides of junction
  (2) smaller depletion region
Therefore the width of depletion region will become smaller

## Slide 84: Forward-Bias Case Width of Depletion Region
W = Width of the depletion region
εs = Electrical permeability of Silicon
q= magnitude of electron charge
NA= concentration of acceptor atoms
ND= concentration of donor atoms
V0= barrier/junction built in voltage
VF = externally applied voltage

## Slide 85: Forward-Bias Case Magnitude of the Junction Capacitor
A= cross sectional area of the junction
εs = Electrical permeability of Silicon
q= magnitude of electron charge
NA= concentration of acceptor atoms
ND= concentration of donor atoms
V0= barrier/junction built in voltage
VF = externally applied voltage

## Slide 86: 3.5.2. The Current-Voltage Relationship of the Junction
Q: What happens, exactly, when a forward-bias voltage (VF) is applied to the pn-junction?
  step #1: Initially, a small forward-bias voltage (VF) is applied.
  Because of its polarity, it pushes majority carriers (holes in p-region and electrons in n-region) toward the junction thereby reducing the width of the depletion zone.
    Note, however, that this force is opposed by the built-in voltage built in voltage V0.

## Slide 87: step #1: Initially, a small forward-bias voltage (VF) is applied. because of its polarity, it pushes majority (holes in p-region and electrons in n-region) toward the junction and reduces width of the depletion zone.
Figure: The pn junction with applied voltage.
VF
Note that, in this figure, the smaller circles represent minority carriers and not bound charges – which are not considered here.

## Slide 88: step #2: As the magnitude of VF increases, the depletion zone becomes thin enough such that the barrier voltage (V0 – VF) can no longer stop diffusion current
Figure: The pn junction with applied voltage.
VF
Note that removing barrier voltage does not facilitate diffusion, it only removes the electromotive force which opposes it.

## Slide 89: step #3: Majority carriers (free electrons in n-region and holes in p-region) cross the junction and become minority charge carriers in the near-neutral region.
Figure: The pn junction with applied voltage.
diffusion current (ID)
drift current (IS)
VF

## Slide 90: step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
Figure: The pn junction with applied voltage.
minority carrier concentration
location (x)
VF

## Slide 91: step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
Figure: The pn junction with no applied voltage (open-circuited terminals).
VF
minority carrier concentration
location (x)

## Slide 92: step #5: Diffusion current is maintained – in spite low diffusion lengths (e.g. microns) and recombination – by constant flow of both free electrons and holes towards the junction.
Figure: The pn junction with no applied voltage (open-circuited terminals).
VF
flow of holes
flow of electrons
flow of diffusion current (ID)
recombination

## Slide 93: 3.5.2. The Current-Voltage Relationship of the Junction
step #1: Initially, a small forward-bias voltage (VF) is applied. because of its polarity, it pushes majority (holes in p-region and electrons in n-region) toward the junction and reduces width of the depletion zone.
step #2: As the magnitude of VF increases, the depletion zone becomes thin enough such that the barrier voltage (V0 – VF) can no longer stop diffusion current

## Slide 94: 3.5.2. The Current-Voltage Relationship of the Junction
step #3: Majority carriers (free electrons in n-region and holes in p-region) cross the junction and become minority charge carriers in the near-neutral region.
step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
step #5: Diffusion current is maintained – in spite low diffusion lengths (e.g. microns) and recombination – by constant flow of both free electrons and holes towards the junction.

## Slide 95: 3.5.2. The Current-Voltage Relationship of the Junction
Q: For forward-biased case, how is diffusion current (ID) defined?
  step #1: Take derivative of (3.35) to define component of diffusion current attributed to flow of holes.

## Slide 96: 3.5.2. The Current-Voltage Relationship of the Junction
Q: For forward-biased case, how is diffusion current (ID) defined?
  step #2: Note that this value is maximum at x = xn.

## Slide 97: Q: For forward-biased case, how is diffusion current defined?
  step #3: Define the component of maximum diffusion current attributed to minority-carrier electrons – in method similar above.

## Slide 98
step #4: Define total diffusion current as sum of components attributed to free electrons and holes.
Q: For forward-biased case, how is diffusion current defined?

## Slide 99
step #4: Define total diffusion current as sum of components attributed to free electrons and holes.
Q: For forward-biased case, how is diffusion current defined?

## Slide 100: 3.5.2. The Current-Voltage Relationship of the Junction
Q: For forward-biased case, how is diffusion current (ID) defined?
  A: Refer to (3.40). This is a very important equation which will be employed in future chapters.

## Slide 101: 3.5.2. The Current-Voltage Relationship of the Junction
Forward-biased diffusion current (ID)
A: Cross sectional surface of a portion of a semi-conductor material (m2)
q: Charge (Coulomb)
ni: Number of electrons across the cross sectional surface (no units)
Dp, Dn: Diffusion constant for holes (p) and electrons (n) (number of charge particules/m3/s)
Lp, Ln: hole and electron Diffusion Lengths (m)
ND, NA: Doping concentration across the cross sectional surface

## Slide 102: 3.5.2. The Current-Voltage Relationship of the Junction
saturation current (IS) – is the maximum reverse current which will flow through pn-junction.
Figure 3.13: The pn junction I–V characteristic.

## Slide 103: 3.5.2. The Current-Voltage Relationship of the Junction
saturation current (IS) – is proportional to:
  cross-section of junction (A).
  Typical value is 10-18A.
  Meaning that is typically a small negative current

## Slide 104: Summary (1)
Today’s microelectronics technology is almost entirely based on the semiconductor silicon. If a circuit is to be fabricated as a monolithic integrated circuit (IC), it is made using a single silicon crystal, no matter how large the circuit is.
In a crystal of intrinsic or pure silicon, the atoms are held in position by covalent bonds. At very low temperatures, all the bonds are intact; No charge carriers are available to conduct current. As such, at these low temperatures, silicone acts as an insulator.

## Slide 105: Summary (2)
At room temperature, thermal energy causes some of the covalent bonds to break, thus generating free electrons and holes that become available to conduct electricity.
Current in semiconductors is carried by free electrons and holes. Their numbers are equal and relatively small in intrinsic silicon.
The conductivity of silicon may be increased drastically by introducing small amounts of appropriate impurity materials into the silicon crystal – via process called doping.

## Slide 106: Summary (3)
There are two kinds of doped semiconductor: n-type in which electrons are abundant, p-type in which holes are abundant.
There are two mechanisms for the transport of charge carriers in a semiconductor: drift and diffusion.
Carrier drift results when an electric field (E) is applied across a piece of silicon. The electric field accelerates the holes in the direction of E and electrons oppositely. These two currents sum to produce drift current in the direction of E.

## Slide 107: Summary (4)
Carrier diffusion occurs when the concentration of charge carriers is made higher in one part of a silicon crystal than others. To establish a steady-state diffusion current, a carrier concentration must be maintained in the silicon crystal.
A basic semiconductor structure is the pn-junction. It is fabricated in a silicon crystal by creating a p-region in proximity to an n-region. The pn-junction is a diode and plays a dominant role in the structure and operation of transistors.

## Slide 108: Summary (5)
When the terminals of the pn-junction are left open, no current flows externally. However, two equal and opposite currents (ID and IS) flow across the junction. Equilibrium is maintained by a built-in voltage (V0). Note, however, that the voltage across an open junction is 0V, since V0 is cancelled by potentials appearing at the metal-to-semiconductor connection interfaces.
The voltage V0 appears across the depletion region, which extends on both sides of the junction.

## Slide 109: Summary (6)
The drift current IS is carried by thermally generated minority electrons in the p-material that are swept across the depletion region into the n-side. The opposite occurs in the n-material. IS flows from n to p, in the reverse direction of the junction. Its value is a strong function of temperature, but independent of V0.
Forward biasing of the pn-junction, that is applying an external voltage that makes p more positive than n, reduces the barrier voltage to V0 - V and results in an exponential increase in ID (while IS remains unchanged).

## Slide 110: Summary (7)
The drift current IS is carried by thermally generated minority electrons in the p-material that are swept across the depletion region into the n-side. The opposite occurs in the n-material. IS flows from n to p, in the reverse direction of the junction. Its value is a strong function of temperature, but independent of V0.
Forward biasing of the pn-junction, that is applying an external voltage that makes p more positive than n, reduces the barrier voltage to V0 - V and results in an exponential increase in ID (while IS remains unchanged).

## Slide 111: Homework
Review problem 3.6 on p151
Review table on pages 159-160
Do problems 3.20, 3.21, 3.22

## Slide 112: 3.1. Intrinsic Semiconductors
thermal generation – effects a equal concentration of free electrons and holes.
  Therefore, electrons move randomly throughout the material.
In thermal equilibrium, generation and recombination rates are equal.

## Slide 113: Workshop Exercises
Exercise 7
The junction capacitance for VR=1V is then found to be
For VR=5V
Comment: The magnitude of the junction capacitance is usually at or
below the pico Farad range, and it decreases as the reverse-bias
voltage increases.